## Slide 1: Capabilities & MOPex
draft-ietf-roll-capabilities
draft-ietf-roll-mopex

## Slide 2: Updates
Splitup between Capabilities and MOPex
Capabilities draft update
  Recommendations for adding new caps
Specific capability instances added
  For 6LoRH
  For PDAO (DAO projection)
Security Considerations
  Still needs more work
Added Rabi as co-author (thanks to his contributions on defining new instances)
References fixed

## Slide 3: MOPex
Problem statement and requirement was already discussed on WG
  MOPs exhausted
  Reserving MOP=7
Minimal document with clear motivation/proposition
Working group adopted
Notes: - DAO-projection or AODV-RPL both cannot proceed without solving this issue.
-

## Slide 4: RPL2: New Options and backward compatibility
Every time a new draft introduces a new option, we have backward compatibility issue
Problem stems from the fact that legacy nodes will strip off this new unknown option
This is true for: Enrollment-priority, Eliding-options, NSA extensions
Solution
  Handle this in MOPex
  Option type with MSB set MUST be copied. Applicable to DIO/DAO.
  0 to 127 → Regular Options (strip off if not understood)
  127 to 255 → Options to copy forward if not understood.
    Enrollment-priority could be Option Type 127
Does not incur any new overhead

## Slide 5: Capabilities Updates
How are capabilities different?
  Compared to MOP, Configuration Option or Routing Metrics/Constraints
Guidelines towards defining new capabilities
  How to set Global/Info/Join-as-leaf flags?
  How should a node handle the capability it does not support?
    Before or After joining the instance
  When to use and when not to use caps.

## Slide 6: Global vs Local Capabilities
Global capabilities
  Only root can set and applicable for the RPL Instance
  Intermediate 6LRs MUST copy these caps in their DIOs
  A node may join as 6LR or 6LN depending on ‘J’ bit of the capability
    Even if the Global capability is not understood by the node
    This allows a Global cap to be optional for the node to understand
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| CAPType |J|I|G|C|.|.|.|.| CAPInfo(Opt)
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 7: New Capability: Capability Indicators
Two types of capabilities
  Feature, singular function either supported or not
    Aim to group all such indicators into a single option
  Feature with additional information
Capability Indicators group together all singular functions
  For e.g., 6LoRH (Note the ‘T’ flag in the below diagram)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type=0x01 |J|I|G|C|. . . .| Len=3 |. . . . . Indic|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|ators . . . . . . . . . . . .|T|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 8: New capability: Routing Resource Capability
Useful for P-DAO
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type=0x03 |J|I|G|C|. . . .| CAPLen | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Total Capacity |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+